## Slide 1: The proposal of calculating contact force between two convex objects by 6 DoF constraints （6自由度拘束による接触力計算手法の提案）
18M14598
M1 Kim SaeYoung

## Slide 2: Index
Backgrounds
What is the simulation based on analytical method
How to calculate the contact in simulation based on analytical method
The problem of using calculating method based on contact point
The problem of conventional method
The problem of related work
Purpose
Proposal
Experiment
Conclusion
Future work
Appendix A. Zero moment point(ZMP)
Appendix B. The data of Experiment
Appendix C. Dynamical scene
Appendix D. The Algorithm of finding the closest point from constrained ZMP
Appendix E. Euclidean projection

## Slide 3: Background
The physics engine plays the role to give autonomy to virtual world
There is close relationship between physics engine and virtual word(for example, Real-time property etc.).
Recent physics engine use the analytical method for simulation

## Slide 4: What is the simulation based on analytical method (1)
The simultaneous equation are formulated by the motion of two objects.
From physical constraints, this equation can be Linear Complementarity Problem (LCP).
It is possible to get the resolution of two objects` motion (Impulses , relative velocities and angular velocities from impulses) on next time.

## Slide 5: What is the simulation based on analytical method (2)
Simultaneous equation
(:the relative velocities/angular velocities between two objects,
:the impulses between two objects)
The constraints
Figure 1 example of contact between two objects
Notes: とがっていることが論理

## Slide 6: How to calculate the contact in simulation based on analytical method
The conventional method to calculate the contact, (1) Calculate the contact manifold from two objects when there is collision between them (2) Solve the simultaneous equations generated from each vertex by using physical constraints(equally, resolve the impulse and velocities based on contact point)
Figure 2 The contact manifold generated from contact between two objects
Notes: 半透明なものはちゃんと書く！線を

## Slide 7: The problem of using calculating method based on contact points (1)
Method of calculating simultaneous equation based on contact points causes processing time to increase
Figure 3 The relation between The number of contact points and The number of simultaneous equation
Page 10

## Slide 8: The problem of using calculating method based on contact points (2)
Method of calculating simultaneous equation based on contact points causes ambiguity to set appropriate contact points when Convex object with shape of curve is collided
Figure 4 The contact manifold between cylinder and box

## Slide 9: The problem of conventional method (1)
The conventional method regards cylinder as the object with shape of polygon.
But This method cause motion different from ideal moving when using polygon cylinder.
Movie 1 The example of different moving (72 polygon)

## Slide 10: The problem of conventional method (2)
From The problem of using calculating method based on contact points (1)(page 7), this method also can make the calculation time to increase when cylinder is used in simulation
Figure 5 the contact manifold of Polygon cylinder

## Slide 11: The problem of related work (1)
6D Frictional Contact for Rigid Bodies [1]
  Purpose : Rolling and spinning cannot be calculated from one contact point in conventional method. So, this research purpose how to calculate the rolling and spinning torque from only one contact point.

## Slide 12: The problem of related work (2)
This research use concept of CoP(center of pressure) and calculate the intersection shape for projection of CoP by using GPU
In case of creating the computer games, for general diffusion, the simulation without GPU has possibility to increase market competitiveness

## Slide 13: Purpose
(1) To propose calculating method of the contact between two object based on contact surface without using GPU.
(2) To keep the fidelity of motion and decrease the processing time compared to conventional method.

## Slide 14: Comparison between conventional method and proposal (1)
Figure 6 The process of calculating contact force and torque
Collsion detection
Simultaneous equation
Calculating
constraint force &
constraint torque
Renewing
velocities and position
The steps of
recursion formula
Projection by constraints
Iterative method

## Slide 15: Comparison between conventional method and proposal (2)
Constraints | Conventional method （based on contact points） | Proposal （based on contact surface）
Constraints on force |  | 
Constraints on torque |  | + Constraints by Zero Moment Point (ZMP)
Constraints | Conventional method （based on contact points） | Proposal （based on contact surface）
Constraints on force |  | 
Constraints on torque |  | 
Table 1 Comparison between conventional method and proposal
Notes: 接触点と接触面に基づいたときの計算する点の数が変わるという図と表を一緒に見せる。
・・ ここからスタート（PESummit）

## Slide 16: Proposal (1)
To set the relative angular velocities will be 0 only can cause unnatural motion
Unnatural motion means that the object don`t tumble down like figure 7
Figure 7 The example of unnatural motion

## Slide 17: Proposal (2)
Unnatural moving is generated from binding relative angular velocities ONLY
For removing unnatural moving, we find the condition whether object falls down or not
This condition can be generated by calculating Zero Moment Point (ZMP)

## Slide 18: Constraint by ZMP (1)
ZMP means that the point with respect to reaction force
The sum of moment is 0 on ZMP
ZMP must exist on contact manifold
Figure 8 The example of ZMP

## Slide 19: Constraint by ZMP (2)
If ZMP exists out of contact manifold, the object must fall down.
The motion between two objects can be predicted by using Where ZMP exists (inside or outside contact manifold)
Figure 9 The relation between motion and ZMP

## Slide 20: Constraint by ZMP (3)
To calculate ZMP if there is no falling down (equally, constraint angular velocity)
Figure 10 How to calculate ZMP
p
Notes: この説明もいる

## Slide 21: Proposal (3)
Contact state judging algorithm
The closet point finding algorithm

## Slide 22: Proposal (4)
Contact state judging algorithm can help to detect whether contact manifold exists or not
Figure 11 The example of judging contact state

## Slide 23: Proposal (5)
(1) surface to surface
(2) surface to point
Figure 12 the case of contact state

## Slide 24: Proposal (6)
the closet point finding algorithm can help to where the ZMP must be moved
In my research, the concept of support point is used for finding the closet point, and this algorithm is generic for only convex objects
Figure 13 example of finding the closest point

## Slide 25: Proposal (7)
But, there are two candidates for moving ZMP because we don`t know any information of contact manifold.
(1) Contact manifold is generated from contact between two objects, so contact manifold must be contained with two objects
(2) ZMP must exist in contact manifold
(3) ZMP must be contained with two objects

## Slide 26: Proposal (8)
２
１
// Step 1
If()
break;
←The closest point on object 1 from ZMP
←The closest point on object 2 from ZMP
if ()
move ZMP to
else if ()
move ZMP to
else //
move to step 2
Figure 14 the example of step 1
Figure 15 Pseudo code of step 1

## Slide 27: Proposal (9)
２
１
Figure 16 The example of step 2
Stop
Yes
ZMP
The closest point from object 1
The closest point from object 2
Distance between two points smaller than constant
The closest point from object 1
The closest point from object 2
No
Figure 17 The process of step 2
Page 40
Notes: 話はすべきうまく。
簡略的でもアルゴリズム信頼性がない
アニメでどのように動いていくかを説明すべき

## Slide 28: Evaluation (1)
Physics engine : Springhead2
Intel® Core™ i5-8250U 1.60GHz
Iteration number of calculating LCP : 15
60Hz
Acceleration of gravity :
Box ()
Cylinder ()
Cylinder (36 Polygon, 54 Polygon, 72 Polygon) ()

## Slide 29: Evaluation (2)
The scenes for evaluation (1) Cylinder is just on the ground (2) Cylinder fall down when contact is as to edge contact (3) Cylinder fall down when contact is as to point contact
Evaluation parts (1) Fidelity (by tracking the change of velocities in dynamical scene) (2) Calculation time (by measuring time for contact analysis and contact force calculation)

## Slide 30: Evaluation (3)
Figure 18 the example that cylinder is just on ground

## Slide 31: Evaluation (4)
1.2m
Figure 19 the example that cylinder fall down when contact is as to edge contact

## Slide 32: Evaluation (5)
1.25m
1.25m
Figure 20 the example that cylinder fall down when contact is as to point contact

## Slide 33: Evaluation (Calculation time-1)
Chart: Calculation time (Cylinder is just on ground)
| Cylinder | 36 Polygon | 54 Polygon | 72 Polygon
Contact analysis | 2.0576 | 19.893 | 32.377 | 50.994
Calculation contact force/torque | 4.9055 | 17.1935 | 23.9278 | 31.3345
Figure 21 The result of calculation time
(Cylinder falls down – Edge contact)
Movie 2 Just on ground

## Slide 34: Evaluation (Calculation time-2)
Chart: Calculation time (cylinder falls down - Edge contact)
| Cylinder | 36 Polygon | 54 Polygon | 72 Polygon
Contact analysis | 6.2355 | 11.5433 | 16.3032 | 16.7607
Calculation contact force/torque | 3.095 | 2.4031 | 2.6145 | 2.2817
Figure 22 The result of calculation time
(Cylinder falls down – Edge contact)
Movie 3 falling down with edge contact

## Slide 35: Evaluation (Calculation time-3)
Chart: Calculation time (cylinder falls down - point contact)
| Cylinder | 36 Polygon | 54 Polygon | 72 Polygon
Contact analysis | 5.9558 | 6.5865 | 8.806 | 10.8211
Calculation contact force/torque | 2.7515 | 1.7544 | 1.7843 | 1.8324
Figure 23 The result of calculation time
(Cylinder falls down – point contact)
Movie 4 falling down with point contact

## Slide 36: Evaluation (Fidelity-1)
Chart: The change of cylinder`s angular velocity (edge contact)
Figure 24 The result of change of cylinder`s angular velocity (edge contact)

## Slide 37: Evaluation (Fidelity-2)
Chart: The change of cylinder`s angular velocity (point contact)
Figure 25 The result of change of cylinder`s angular velocity (point contact)

## Slide 38: Conclusion
The result of Evaluation show that this research has meaningful result at the scene stop position and falling down when contact is as to edge contact compared to conventional method
But, at the scene falling down when contact is as to point contact, The calculation contact force/torque time of 36 Polygon cylinder is more faster than calculation time using this research
Because, proposal method use complex algorithms (contact state judging and the closest point finding algorithm) in calculating contact force/torque compared to conventional method

## Slide 39: Future work (1)
Implement the algorithm which find the closest point onto two convex objects and give fast convergence rates
Stabilization

## Slide 40: Future work (2)
In my research, my algorithm for finding the closest point onto two convex objects is different from Euclidean Projection [2] (Appendix E)(Page 27)
this method assume that there are only two convex objects.
There is research paper to general object(nonconvex object) [3]

## Slide 41: Future work (3)
Movie 5 the stack of cylinder

## Slide 42: Future work (4)
So, there is method for stabilization to frozen these objects when the velocity of individual objects is smaller than standard speed.
But in springhead2, to frozen the object cannot be work now.
To change the value of freezezthreshold in SprPHEngine.h and use the function SetFrozen in UpdateVelocity function (PHSolid.cpp) both cannot be worked.

## Slide 43: Future work (5)
If the only rule to frozen two objects by using the individual velocities, the tipping like moive 3 cannot be occurred
in stabilization in scene of stack of objects, it is important to calculate the axis of contact
From these facts, I must think two things : (1) how to frozen objects (the rule) (2) how to calculate the axis of contact
Movie 6 Tipping

## Slide 44: Appendix A The data of Experiment (1)
Chart: Entire calculation time (Cylinder falls down – Edge contact)
Figure 26 The graph of entire calculation time (Cylinder falls down – Edge contact)

## Slide 45: Appendix A The data of Experiment (2)
Chart: Contact analysis calculation time (Cylinder falls down – Edge contact)
Figure 27 The graph of contact analysis calculation time (Cylinder falls down – Edge contact)

## Slide 46: Appendix A The data of Experiment (3)
Chart: Contact force/torque calculation time (Cylinder falls down – Edge contact)
Figure 28 The graph of contact force/torque calculation time (Cylinder falls down – Edge contact)

## Slide 47: Appendix A The data of Experiment (4)
Chart: Entire calculation time (Cylinder falls down – Point contact)
Figure 29 The graph of entire calculation time (Cylinder falls down – Point contact)

## Slide 48: Appendix A The data of Experiment (5)
Chart: Contact analysis calculation time (Cylinder falls down – Point contact)
Figure 30 The graph of contact analysis calculation time (Cylinder falls down – Point contact)

## Slide 49: Appendix A The data of Experiment (6)
Chart: Contact force/torque calculation time (Cylinder falls down – Point contact)
Figure 31 The graph of contact force/torque calculation time (Cylinder falls down – Point contact)

## Slide 50: Appendix A The data of Experiment (7)
Chart: Entire calculation time (Cylinder is just on ground)
Figure 32 The graph of entire calculation time (Cylinder is just on ground)

## Slide 51: Appendix A The data of Experiment (8)
Chart: Contact analysis calculation time (Cylinder is just on ground)
Figure 33 The graph of contact analysis calculation time (Cylinder is just on ground)

## Slide 52: Appendix A The data of Experiment (9)
Chart: Contact force/torque calculation time (Cylinder is just on ground)
Figure 34 The graph of contact force/torque calculation time (Cylinder is just on ground)

## Slide 53: Appendix B Dynamical scene (1)
Movie 7 the collision with 3 objects (1)

## Slide 54: Appendix B Dynamical scene (2)
Movie 8 the collision with 3 objects (2)

## Slide 55: Appendix B Dynamical scene (3)
Movie 9 Rolling cylinder

## Slide 56: Appendix C The Algorithm of finding the closest point from constrained ZMP (1)
Support point
p
Figure 35 Support point

## Slide 57: Appendix C The Algorithm of finding the closest point from constrained ZMP (2)
Finding the closest point from support point
Extract random point on object
From point generated step 1(point 1), draw the vector p1 which is point 1 to ZMP
Calculate S(p1)
If calculated point from step 2(point 2) is the same point 1, point 1 will be the closest point from ZMP
Draw the vector p2 which is point 2 to ZMP
Calculate S(p2)
Draw the line segment that ends of line segment are p1 and p2 (line 1), draw the vector(p3) from line1 to ZMP
Calculate S(p3)
If calculate point from step 8(point 3) is the same point from step 3 or 6, point 3 will be the closest point from ZMP
Figure 36 The simple example of the closest point finding algorithm

## Slide 58: Appendix C The Algorithm of finding the closest point from constrained ZMP (3)
pt ← ZMP – the random point on object
Simplex = {} ← the set of Simplex
tmp ← S(pt)
while(1){
if(S(pt) exists in Simplex) return tmp;
else
switch(Simplex.number()){
case 0 : Simplex.add(S(pt)) && pt ← ZMP – S(pt)
case 1 : Simplex.add(S(pt)) && pt ← Vector from simplex(line segment) to ZMP
&& tmp = The starting point of pt (on the simplex)
case 2 : Simplex.add(S(pt)) && pt ← Vector from simplex（triangle） to ZMP
&& tmp = The starting point of pt (on the simplex)
case 3 : Simplex.add(S(pt)) && reomove the oldest point in Simplex
&& pt ← Vector from simplex(triangle) to ZMP
&& tmp = The starting point of pt (on the simplex)
}
}
Figure 37 The pseudo code of the closest point finding algorithm
Notes: 点でなくて面で拘束すると何が変わるか

## Slide 59: Appendix D (Zero Moment Point) (1)
Figure 38 Entire state

## Slide 60: Appendix D (Zero Moment Point) (2)
First at all, we think the pointis the point of application and when we assume thatis the contact force on point,has to satisfies the following formulas
(1) The sum of contact force in must be the same. So
So, left side of (1) can be expressed as
From (2), we can rewrite the right side of (1) as

## Slide 61: Appendix D (Zero Moment Point) (3)
(2) The sum of momentum from contact force in must be same the momentum from contact force on point So,
and don’t depend on variable, so (4) can be rewritten by using (2) and (3) as
also don’t depend on variable, So (5) will be rewritten as

## Slide 62: Appendix D (Zero Moment Point) (4)
Now, we think about each items` direction in (6).
We assume that (1)`s direction is . And then we know that is orthogonal to and
We assume that (2)`s direction is . And then we know that is orthogonal to and But and are on the same face (spanned from ) and is orthogonal to this face. From this, is parallel with . And then is orthogonal to . Hence, and have orthogonal relationship.
Now In (6), each items has different directions which have orthogonal relationship and It is 0 when these items sum. Hence, (1) and (2) vector must be .
So, we can say that

## Slide 63: Appendix D (Zero Moment Point) (5)
From (7) , (8) the point of application satisfied that the sum of momentum is 0 on point of application. Also, from these, we can know the concept of ZMP must be used only in Convex object.
Figure 39 The example of Convex and Non-convex
Notes: Non-convex 避けずに
ベクトルを太くしてする

## Slide 64: Appendix E (Euclidean Projection)
1
2
Figure 40 The example of Euclidean projection
Page 40
Notes: 内側でとまるかもしらない。。。